|  |  | Eagle Sirens, Inc. P. O. Box 80705 Lansing, MI 48908-0705 (O) (517) 627-0702 Fax (517) 627-3702 E-Mail: eaglesirens@comcast.net |
| --- | --- | --- |
| September 11, 2001 We Will Remember |  | Electro-Mechanical Sirens for Emergency Vehicles |

# EAGLE SIRENS

# SPECIFICATION SHEET

# ELECTRO-MECHANICAL EAGLE SIRENS

One (1) 12 Volt “Screaming” Eagle Siren # C 9-11-P (Pedestal Mount) electro/mechanical coaster type siren shall be pedestal mounted on the front bumper apron.  The 13.75” L x 6.5” W x 8.5” H siren shall only draw 38 operational amps with a maximum momentary/peak amp draw of 85 amps.

The siren shall produce a focused sound level of 123 decibels.  The Eagle Siren utilizes the unique “Forward Projection System” which creates a uniform pattern of distinct sound waves that motorists immediately identify with that of an approaching emergency vehicle.  By focusing and projecting the sound in a more forward direction and with less sound dispersed to the sides and rear; cab interior decibel levels are lower than those created by conventional electro-mechanical sirens.

Two (2) actuation floor switches shall be provided, one (1) for the officer and one (1) for the driver.

Note: A siren on/off switch shall be installed in the switch panel and wired in such a manner so that when the switch is placed in the off position the siren brakes shall automatically be engaged and the floor switches deactivated.

- Note:  Flush Mounted Siren   When ordering a flush mounted siren, specify ”Screaming” Eagle Siren  # C 9-11-F  (Flush Mount) electro/mechanical coaster type siren.  Siren shall be flush mounted to front bumper.  Dimensions: 12” L x 6.5” H.    Front projection 5.0”,

Rear Projection 6.75”.    Cutout hole: 5.75” diameter.

- Note:  Nesting Eagle Siren   When ordering a nesting eagle mounted siren, specify “Screaming Eagle Nesting Eagle Siren # C 9-11-NE   (Nesting Eagle Mount) electro/mechanical coaster type siren.  Siren shall be mounted behind the bumper with a stainless steel grill mounted on the front of the bumper.

Dimensions: 16” L x 7.25” D x 7.25” H.     Cutout hole: 6” x 6 “.

WARNING:   FAILURE TO WEAR HEARING PROTECTION AND OPERATE  VEHICLE WITH WINDOWS UP CAN INCREASE THE RISK OF TEMPORARY OR PERMANENT HEARING LOSS